Inclusive Tag-Side Vertex Reconstruction in Partially Reconstructed B decays
-A Progress Report -
11/09/2011 TDBC-BRECO

---
Outline
- Brief Reminder
- Status
- Next Steps

---
Single Tag – CP asymmetry
color yellow{"A"_l (%DELTA t) ~=~ {"N"(bar{B_d}) (%DELTA t)-"N"(B_d)(%DELTA t)} over {"N"(bar{B_d})(%DELTA t) +"N"(B_d)(%DELTA t)} }
color white{%delta = 1 over 2 "A"_{"ll"} = 1 - abs{ q over p}}
color yellow{ ~sim~ %delta ( 1 - cos(%DELTA m %DELTA t) + {%DELTA m } over %GAMMA sin (%DELTA m %DELTA t) )}
- d can be measured as the amplitude of the time-dependent asymmetry
- detector asymmetries can be simultaneously measured as a time independent overall bias
- Different w.r.t. double tag approach, where All is time-independent
Inclusive CP Asymmetries in Semileptonic
Decays of B Mesons
Hitoshi Yamamoto
hep-ph/9707427v2

---
Inclusive Vertex Recosntruction
Event with Ngood tracks selected, consider all permutations of ND “decay” tracks and NO = Ngood-ND other side tracks, compute a likelihood as:
- Choose the combination providing the largest value of L
- Compute the 2nd B vertex from the “other side” tracks selected this way
color white { log "L" ~=~ log "L"( "N"_D "| N"_{good} ) + ~} color white {~+~ log "L"( E_D "|N"_D) + log "L"(cos(%theta_{D,"l"})"|N"_D) + log "L" ("M"_{%nu,D}^2"|N"_D)~+~} color white {~+~ log "L"( E_O "|N"_O) + log "L"(cos(%theta_{ O,"l"})"|N"_O) + log "L" (%PI(Vertex)"|N"_O)~+~} color white {~+~ log "L"( %DELTA E) + log "L"(cos(B_1,B_2))+ log "L"(cos(B,beam)) }

---
Resolution vs true DZ
- Resolution and pull much improved wrt cone cut approach
- Also a sizable efficiency gain (~30% for 90o cone)
color yellow{ Pull : {%DELTA Z_{reco} - %DELTA Z_{true}} over {%sigma(%DELTA Z_meas)} }
color yellow{ %DELTA Z_{reco} - %DELTA Z_{true} }
color blue {%DELTA Z_{true} %element} newline color blue {[-0.25, -0.15]} color blue {[-0.15,-0.10]} color blue {[-0.10,-0.05]} color blue {[-0.025,+0.025]} color blue {[-0.05,-0.025]} color blue {[0.025,0.05]} color blue {[0.15,0.25]} color blue {[0.10,0.15]} color blue {[0.05,0.10]}

---
Validation
- PDFs shapes taken from simulation
- Many variables are involved, individual tuning is time expensive
- Difficult to control correlations
- A posteriori validation :
  - Compare DZ, s(DZ) signal distributions in Data and MC
  - Smear – if necessary – the MC to the data

---
Method
Fit data Squared-Missing-Mass (Mn2) distributions in several bins of the selected variable (e.g. DZ), with the sum of :
color white { ~(1)~ B_d toward D^{"*-"} l^"+" %nu_l }
color white { ~(2)~ B_q toward D^{"**-"} l^"+" %nu_l }
color white { ~(3)~ B_d toward D^{"*-"} l^"+" %nu_l X~~~ }
other peaking, including CP eigenstates
color white { ~(4)~ "Combinatoric "B_d + B_u }
color white { ~(5)~ "Continuum" }
Float (1),(2),(4) . Fix (5) to off-peak events
Compare amount of peaking events (1+2+3) to truth-matched MC in each bin

---
Examples
color yellow{ " Fit Result for Events with"} newline color yellow {~ -0.004 < %DELTA Z < 0.004 }
color yellow{ " Fit Result for Events with"} newline color yellow {~ 0.20 < %DELTA Z < 0.25 }
Squared Missing Mass (GeV2)

---
Results : s(DZ)
        Black Dots : Fitted peaking yield
Colored area : MC

---
Results : Zlepton-ZDecaySide
- DZ computed wrt the tracks assigned to the “other side”, corresponding to the other B meson
- Input for the All measurement
- Good overall agreement

---
Recent Developments
- Fit true Dt distributions for MC events selected as data
- Simultaneous fit to t, Dmd, and n(events) to true signal data splitted by lepton kind, lepton charge, mixing status (8 samples, 10 param.)
       t	1.53790+-0.00066
       Dmd 0.48803+-0.00020
      e+	2674125+-1635
      e-	2626602+-1621
      m+	2355011+-1535
      m-	2314104+-1521
      e+	556471+-746
      e-	547725+-740
      m+	485497+-697
      m-	477249+-691
UNMIXED
MIXED

---
Recent Developments (1)
- Fit true Dt distributions for MC events selected as data
- Simultaneous fit to t, Dmd, and n(events) to true signal data splitted by lepton kind, lepton charge, mixing status (8 samples, 10 param.)
       t	1.53790+-0.00066
       Dmd 0.48803+-0.00020
      e+	2674125+-1635
      e-	2626602+-1621
      m+	2355011+-1535
      m-	2314104+-1521
      e+	556471+-746
      e-	547725+-740
      m+	485497+-697
      m-	477249+-691
UNMIXED
MIXED
Reconstruction asymmetries (%):
 e unmixed	0.896533 0.0436342
  e mixed	0.792013 0.0955594
  e all	0.878514 0.039692
  mu unmixed 0.87612 0.0464871
  mu mixed	0.856674 0.102372
  mu all	0.872795 0.0423274
  lep all	0.875838 0.0289534

---
Recent Developments (2)
- Fit true Dt distributions for MC events selected as data
- Simultaneous fit to t, d, and n(events) to true signal data splitted by lepton kind and lepton charge (4 samples, 6 param.)
      t	1.51756+-0.00062
       Dmd	0.48800+-0.00000 fixed
        d	0.00028+-0.00062
        DG 0.00000+-0.00000 fixed
       e+	3230778+- 1798
       e-	3174548+- 1782
       m+	2840733+- 1686
       m-	2791503+- 1671
Reconstruction asymmetries (%):
  e all	0.877761 0.037217
  mu all	0.874077 0.0423274
  lep all	0.876091 0.0190036

---
Status
- Detector effects induce ~ 0.8% asymmetry in l+p-S vs l-p+S tagging
- Same asymmetry for m and e , probably due to pS reconstruction
- At truth level, it is possible to fit both the CP asymmetry and the individual event rates – i.d. the detector asymmetry (at least for d = 0 )

---
Next Steps
- Prepare MC events with ( +-0.005, +-0.002, +-0.001)
- Check linearity at truth level
- Fit reconstructed simulated events, including resolution effects
- Add background:
  - peaking B+
  - combinatorial
  - continuum
- Toy studies
- Data
color white {%delta <>0 }

---
Conclusion
- Developed a new algorithm to build the “other” vertex in inclusive event
- The method improves sizably wrt the usual cone cut approach:
  - removes the bias
  - improves the overall resolution
- A precision similar to fully reconstructed events can be reached
- The method can be in principle implemented with each partially reconstructed sample (even single leptons)
- CP analysis at start – do not expect fast progresses ...